## Slide 1: hub-spoke with RS in hub and firewall vnet
[October-2024]

## Slide 2: High level diagram
fw-vnet
hub
vnet peering
ER circuit
ER GW1
ER connection
fw-rs1
hub-rs1
nva1
on-prem
eBGP
eBGP
spoke1
vnet peering
fw1-az

## Slide 3: Network diagram
SEA-Cust35-ER
50Mbps
hub-vnet
10.50.0.0/24
workloadSubnet
10.50.0.16/28
RouteServerSubnet
10.50.0.64/26
GatewaySubnet
10.50.0.192/26
On-prem network
10.1.35.0/25
SEA-Cust35-VNet01-gw-er-conn
Web server:
10.1.35.11
10.1.35.12
10.1.35.13
nvaSubnet
10.50.0.0/28
nva1
AS: 65001
.10
hub-rs1
AS:65515
gw-er
SKU: standard
fw-vnet
10.100.0.0/24
workloadSubnet 10.100.0.64/26
fw-vm1
RouteServerSubnet
10.100.0.0/26
spoke1 10.101.0.0/24
fw-rs1
AS:65515
vnet
peering
eBGP
spoke1Subnet 10.101.0.0/25
spok1-vm1
AzureFirewallSubnet
10.100.0.192/26
10.100.0.4,
10.100.0.5
10.50.0.68,
10.50.0.69
.100
10.101.0.10
10.1.35.0/25
ASN: 65020
vnet
peering
eBGP
fw
nva2
AS: 65001
spoke1-RT
Dest net: 0.0.0.0 next-hop: 10.100.0.196
.11
Remote Gateway transit: false
Use Remote Gateways: false
Remote Gateway transit: false
Use Remote Gateways: false
hub-vm1
.20
.196

## Slide 4: route-map in nva1
deny 10.101.0/24
deny 10.100.0.0/24
permit 10.1.35.0/25 BGP next-hop: unchanged
Route Server
fw-rs1
deny 10.100.0.0/24
deny 10.50.0.0/24
permit 10.101.0.0/24 BGP next-hop: IP Az firewall
Route Server
hub-rs1
BGP filter out:
route-map TO-RS-FW
BGP filter out:
route-map TO-RS-HUB
BGP
AS 65001
nva1
BGP advertisements to the RS in the hub:
10.101.0.0/24 BGP next-hop: IP Az firewall
BGP advertisements to the RS in the firewall vnet:
10.1.35.0/25 BGP next-hop: IP RS in hub