## Slide 1: What configuration aims
spoke1
spoke2
hub
vnet2
vnet peering
vnet peering
ER circuit
spoke1
spoke2
hub
vnet2
vnet peering
vnet peering
ER circuit
1. Remove the connection
2. Remove the ER GTW
transit vnet
Vnet2 is used only for transit in case the main ER GW1 and/or conn1 is down
ER GW1
ER GW2
conn2
conn2
conn1
transit vnet
ER GW1
ER GW2

## Slide 2: Full network diagram
SEA-Cust33-ER
Seattle
50Mbps
SEA-Cust34-VNet01
[10.17.34.0/24, 10.0.1.0/24]
tenantSubnet
10.17.34.32/27
RouteServerSubnet
10.0.1.128/25
GatewaySubnet
10.17.34.128/25
spoke1 10.0.50.0/24
SEA-Cust34-vm01
On-prem network
10.1.34.0/25
ASN: 65020
SEA-Cust34-VNet01-gw-er-conn
10.1.33.10
Web server:
10.1.33.10:8080
10.1.33.10:8081
10.1.33.10:8082
SEA-Cust34-VNet02
[10.18.34.0/24,10.0.2.0/24]
RouteServerSubnet
10.0.2.128/25
GatewaySubnet
10.18.34.128/25
SEA-Cust34-nva2
nvaSubnet
10.0.1.0/25
NVASubnet
10.0.2.0/25
vnet
peering
vnet
peering
spoke1Subnet1 10.0.50.0/25
fwSubnet
10.17.34.0/27
UDR-Spoke1
DestNet next-hop
0.0.0.0/0 10.17.34.10
BGP propagation: disabled
IP forwarding
.10
UDR-GTW1
DestNet next-hop
10.0.50.0/24 10.17.33.10
.10
eBGP
eBGP
AS:65001
SEA-Cust34-VNet02-gw2-er-conn
Requested to create a symmetric data path through the SEA-Cust34-fw
SEA-Cust34-fw
SEA-Cust34-rs1
AS:65515
SEA-Cust34-rs2
AS: 65515
SEA-Cust34-VNet01-gw-er
SKU: standard
SEA-Cust34-VNet02-gw-er
SKU: ErGw1AZ
SEA-Cust34-spoke1vm1
10.0.2.132, 10.0.2.133
10.0.1.132, 10.0.1.133
IP forwarding
Requested to create a symmetric data path to/from spoke vnets through SEA-Cust34-fw
westus2
westus3
UDR-GTW2
DestNet next-hop
10.0.50.0/24 10.17.33.10

## Slide 3: Config: failover test
SEA-Cust33-ER
Seattle
50Mbps
SEA-Cust34-VNet01
[10.17.34.0/24, 10.0.1.0/24]
tenantSubnet
10.17.34.32/27
RouteServerSubnet
10.0.1.128/25
GatewaySubnet
10.17.34.128/25
spoke1 10.0.50.0/24
SEA-Cust34-vm01
On-prem network
10.1.34.0/25
ASN: 65020
10.1.33.10
Web server:
10.1.33.10:8080
10.1.33.10:8081
10.1.33.10:8082
SEA-Cust34-VNet02
[10.18.34.0/24,10.0.2.0/24]
RouteServerSubnet
10.0.2.128/25
GatewaySubnet
10.18.34.128/25
SEA-Cust34-nva2
nvaSubnet
10.0.1.0/25
NVASubnet
10.0.2.0/25
vnet
peering
vnet
peering
spoke1Subnet1 10.0.50.0/25
fwSubnet
10.17.34.0/27
SEA-Cust34-nva1
UDR-Spoke1
DestNet next-hop
0.0.0.0/0 10.17.34.10
BGP propagation: disabled
IP forwarding
.10
.10
.10
eBGP
eBGP
AS:65001
SEA-Cust34-VNet02-gw2-er-conn
SEA-Cust34-fw
SEA-Cust34-rs1
AS:65515
SEA-Cust34-rs2
AS: 65515
SEA-Cust34-VNet01-gw-er
SEA-Cust34-VNet02-gw-er
SEA-Cust34-spoke1vm1
10.0.2.132, 10.0.2.133
10.0.1.132, 10.0.1.133
IP forwarding
UDR-nva2
DestNet next-hop
10.0.50.0/24 10.17.33.10
UDR-GTW2
DestNet next-hop
10.0.50.0/24 10.17.33.10
UDR-GTW1
DestNet next-hop
10.0.50.0/24 10.17.33.10

## Slide 4: data path is symmetric
SEA-Cust33-ER
Seattle
50Mbps
SEA-Cust34-VNet01
[10.17.34.0/24, 10.0.1.0/24]
tenantSubnet
10.17.34.32/27
RouteServerSubnet
10.0.1.128/25
GatewaySubnet
10.17.34.128/25
spoke1 10.0.50.0/24
SEA-Cust34-vm01
On-prem network
10.1.34.0/25
ASN: 65020
10.1.33.10
Web server:
10.1.33.10:8080
10.1.33.10:8081
10.1.33.10:8082
SEA-Cust34-VNet02
[10.18.34.0/24,10.0.2.0/24]
RouteServerSubnet
10.0.2.128/25
GatewaySubnet
10.18.34.128/25
SEA-Cust34-nva2
nvaSubnet
10.0.1.0/25
NVASubnet
10.0.2.0/25
vnet
peering
vnet
peering
spoke1Subnet1 10.0.50.0/25
fwSubnet
10.17.34.0/27
SEA-Cust34-nva1
UDR-Spoke1
DestNet next-hop
0.0.0.0/0 10.17.34.10
BGP propagation: disabled
IP forwarding
.10
UDR-GTW1
DestNet next-hop
10.0.50.0/24 10.17.33.10
.10
.10
eBGP
eBGP
AS:65001
SEA-Cust34-VNet02-gw2-er-conn
SEA-Cust34-fw
SEA-Cust34-rs1
AS:65515
SEA-Cust34-rs2
AS: 65515
SEA-Cust34-VNet01-gw-er
SKU: standard
SEA-Cust34-VNet02-gw-er
SKU: ErGw1AZ
SEA-Cust34-spoke1vm1
10.0.2.132, 10.0.2.133
10.0.1.132, 10.0.1.133
IP forwarding
westus2
westus3
UDR-GTW2
DestNet next-hop
10.0.50.0/24 10.17.33.10
1
2
3
4

## Slide 5: Routing with single connection ER circuit vnet02
Connection deleted
SEA-Cust34-VNet01-gw-er-conn
SEA-Cust34-VNet02-gw2-er-conn: UP
SEA-Cust34-spoke1vm1-nic
VM in spoke vnet does not see the on-premises network
All traffic with destination different from address space vnet1 is managed goes to virtual appliance 10.17.34.10
SEA-Cust34-vm1-nic
SEA-Cust34-fw (10.17.34.10) has in the on-premises network 10.1.34.0/25
The on-premises route has next-hop, the IP address the route server (10.0.2.132) in vnet02
Source | State | Address Prefixes | Next Hop Type | Next Hop IP Address | User Defined Route Name
Default | Active | 10.0.50.0/24 | Virtual network |  | 
Default | Active | 10.17.34.0/24 | VNet peering |  | 
Default | Active | 10.0.1.0/24 | VNet peering |  | 
Default | Invalid | 0.0.0.0/0 | Internet |  | 
User | Active | 0.0.0.0/0 | Virtual appliance | 10.17.34.10 | to-fwVM
Source | State | Address Prefixes | Next Hop Type | Next Hop IP Address | User Defined Route Name
Default | Active | 10.17.34.0/24 | Virtual network |  | 
Default | Active | 10.0.1.0/24 | Virtual network |  | 
Default | Active | 10.0.50.0/24 | VNet peering |  | 
Virtual network gateway | Active | 10.1.34.0/25 | Virtual network gateway | 10.0.2.132 | 
Default | Active | 0.0.0.0/0 | Internet |  | 
Default | Active | 10.18.34.0/24 | VNetGlobalPeering |  | 
Default | Active | 10.0.2.0/24 | VNetGlobalPeering |  | 

## Slide 6
SEA-Cust34-nva2-nic
Source | State | Address Prefixes | Next Hop Type | Next Hop IP Address | User Defined Route Name
Default | Active | 10.18.34.0/24 | Virtual network |  | 
Default | Active | 10.0.2.0/24 | Virtual network |  | 
Virtual network gateway | Active | 10.1.34.0/25 | Virtual network gateway | 10.3.129.52 | 
Virtual network gateway | Active | 10.0.50.0/24 | Virtual network gateway | 10.0.1.132 | 
Default | Active | 0.0.0.0/0 | Internet |  | 
Default | Active | 10.17.34.0/24 | VNetGlobalPeering |  | 
Default | Active | 10.0.1.0/24 | VNetGlobalPeering |  | 

## Slide 7: Route server rs1
Get-AzRouteServerPeerLearnedRoute -ResourceGroupName SEA-Cust34 -RouteServerName SEA-Cust34-rs1 -PeerName bgp-conn1 | ft
LocalAddress Network NextHop SourcePeer Origin AsPath Weight
------------ ------- ------- ---------- ------ ------ ------
10.0.1.133 10.0.2.0/24 10.0.2.132 10.0.2.10 EBgp 65001-65001 32768
10.0.1.133 10.18.34.0/24 10.0.2.132 10.0.2.10 EBgp 65001-65001 32768
10.0.1.133 10.1.34.0/25 10.0.2.132 10.0.2.10 EBgp 65001-65001-12076-65020 32768
10.0.1.132 10.18.34.0/24 10.0.2.132 10.0.2.10 EBgp 65001-65001 32768
10.0.1.132 10.0.2.0/24 10.0.2.132 10.0.2.10 EBgp 65001-65001 32768
10.0.1.132 10.1.34.0/25 10.0.2.132 10.0.2.10 EBgp 65001-65001-12076-65020 32768
Get-AzRouteServerPeerAdvertisedRoute -ResourceGroupName SEA-Cust34 -RouteServerName SEA-Cust34-rs1 -PeerName bgp-conn1 | ft
LocalAddress Network NextHop SourcePeer Origin AsPath Weight
------------ ------- ------- ---------- ------ ------ ------
10.0.1.133 10.17.34.0/24 10.0.1.133 Igp 65515 0
10.0.1.133 10.0.1.0/24 10.0.1.133 Igp 65515 0
10.0.1.133 10.0.50.0/24 10.0.1.133 Igp 65515 0
10.0.1.132 10.17.34.0/24 10.0.1.132 Igp 65515 0
10.0.1.132 10.0.1.0/24 10.0.1.132 Igp 65515 0
10.0.1.132 10.0.50.0/24 10.0.1.132 Igp 65515 0
SEA-Cust34-nva2
AS:65515
SEA-Cust34-rs1
AS:65001
SEA-Cust34-nva2
AS:65515
SEA-Cust34-rs1
AS:65001
10.1.34.0/25 {65001-65001-12076-65020}
10.0.50.0/24 {65515}
10.17.34.0/24 {65515}
10.0.1.0/24 {65515}
10.18.34.0/24 {65001-65001}
10.0.2.0/24 {65001-65001}

## Slide 8: Route server rs2
Get-AzRouteServerPeerLearnedRoute -ResourceGroupName SEA-Cust34 -RouteServerName SEA-Cust34-rs2 -PeerName bgp-conn1 | ft
LocalAddress Network NextHop SourcePeer Origin AsPath Weight
------------ ------- ------- ---------- ------ ------ ------
10.0.2.132 10.0.50.0/24 10.0.1.132 10.0.2.10 EBgp 65001-65001 32768
10.0.2.132 10.0.1.0/24 10.0.1.132 10.0.2.10 EBgp 65001-65001 32768
10.0.2.132 10.17.34.0/24 10.0.1.132 10.0.2.10 EBgp 65001-65001 32768
10.0.2.133 10.0.50.0/24 10.0.1.132 10.0.2.10 EBgp 65001-65001 32768
10.0.2.133 10.0.1.0/24 10.0.1.132 10.0.2.10 EBgp 65001-65001 32768
10.0.2.133 10.17.34.0/24 10.0.1.132 10.0.2.10 EBgp 65001-65001 32768
Get-AzRouteServerPeerAdvertisedRoute -ResourceGroupName SEA-Cust34 -RouteServerName SEA-Cust34-rs2 -PeerName bgp-conn1 | ft
LocalAddress Network NextHop SourcePeer Origin AsPath Weight
------------ ------- ------- ---------- ------ ------ ------
10.0.2.132 10.18.34.0/24 10.0.2.132 Igp 65515 0
10.0.2.132 10.0.2.0/24 10.0.2.132 Igp 65515 0
10.0.2.132 10.1.34.0/25 10.0.2.132 Igp 65515-12076-65020 0
10.0.2.133 10.18.34.0/24 10.0.2.133 Igp 65515 0
10.0.2.133 10.0.2.0/24 10.0.2.133 Igp 65515 0
10.0.2.133 10.1.34.0/25 10.0.2.133 Igp 65515-12076-65020 0
SEA-Cust34-nva2
AS:65515
SEA-Cust34-rs2
AS:65001
SEA-Cust34-nva2
AS:65515
SEA-Cust34-rs2
AS:65001
10.0.1.0/24 {65001-65001}
10.17.34.0/24 {65001-65001}
10.0.50.0/24 {65001-65001}
10.1.34.0/25 {65515-12076-65020}

## Slide 9: ER gateway in vnet02
Get-AzVirtualNetworkGatewayAdvertisedRoute -VirtualNetworkGatewayName SEA-Cust34-VNet02-gw-er -ResourceGroupName SEA-Cust34 -Peer 10.18.34.132 | ft
LocalAddress Network NextHop SourcePeer Origin AsPath Weight
------------ ------- ------- ---------- ------ ------ ------
10.18.34.141 10.18.34.0/24 10.18.34.141 Igp 65515 0
10.18.34.141 10.0.2.0/24 10.18.34.141 Igp 65515 0
10.18.34.141 10.0.50.0/24 10.18.34.141 Igp 65515-65001-65001 0
10.18.34.141 10.17.34.0/24 10.18.34.141 Igp 65515-65001-65001 0
10.18.34.141 10.0.1.0/24 10.18.34.141 Igp 65515-65001-65001 0
SEA-Cust34-VNet02-gw-er
SEA-Cust34-rs2
SEA-Cust34-VNet02-gw2-er-conn
AS:65515
SEA-Cust34-VNet02-gw-er
SEA-Cust34-rs2
AS:65515
10.1.34.0/25 {12076-65020}
10.0.50.0/24 {65001-65001}
10.17.34.0/24 {65001-65001}
Get-AzVirtualNetworkGatewayLearnedRoute -VirtualNetworkGatewayName SEA-Cust34-VNet02-gw-er -ResourceGroupName SEA-Cust34 | ft
LocalAddress Network NextHop SourcePeer Origin AsPath Weight
------------ ------- ------- ---------- ------ ------ ------
10.18.34.141 10.18.34.0/24 10.18.34.141 Network 32768
10.18.34.141 10.0.2.0/24 10.18.34.141 Network 32768
10.18.34.141 10.1.34.0/25 10.18.34.132 10.18.34.132 EBgp 12076-65020 32769
10.18.34.141 10.1.34.0/25 10.18.34.133 10.18.34.133 EBgp 12076-65020 32769
10.18.34.141 10.0.50.0/24 10.0.1.132 10.0.2.132 IBgp 65001-65001 32768
10.18.34.141 10.0.50.0/24 10.0.1.132 10.0.2.133 IBgp 65001-65001 32768
10.18.34.141 10.17.34.0/24 10.0.1.132 10.0.2.132 IBgp 65001-65001 32768
10.18.34.141 10.17.34.0/24 10.0.1.132 10.0.2.133 IBgp 65001-65001 32768
10.18.34.141 10.0.1.0/24 10.0.1.132 10.0.2.132 IBgp 65001-65001 32768
10.18.34.141 10.0.1.0/24 10.0.1.132 10.0.2.133 IBgp 65001-65001 32768
10.18.34.141 10.1.34.0/25 10.18.34.132 10.0.2.132 IBgp 12076-65020 32768
10.18.34.141 10.1.34.0/25 10.18.34.132 10.0.2.133 IBgp 12076-65020 32768

## Slide 10: Routing ER circuit
Network | Next hop | LocPrf | Weight | Path
10.0.1.0/24 | 10.18.34.141 |  | 0 | 65515 65001 65001
10.0.1.0/24 | 10.18.34.140* |  | 0 | 65515 65001 65001
10.0.2.0/24 | 10.18.34.140 |  | 0 | 65515
10.0.2.0/24 | 10.18.34.141* |  | 0 | 65515
10.0.50.0/24 | 10.18.34.141 |  | 0 | 65515 65001 65001
10.0.50.0/24 | 10.18.34.140* |  | 0 | 65515 65001 65001
10.1.34.0/25 | 192.168.34.17 |  | 0 | 65020
10.17.34.0/24 | 10.18.34.141 |  | 0 | 65515 65001 65001
10.17.34.0/24 | 10.18.34.140* |  | 0 | 65515 65001 65001
10.18.34.0/24 | 10.18.34.140 |  | 0 | 65515
10.18.34.0/24 | 10.18.34.141* |  | 0 | 65515
SEA-Cust33-ER-primary link
Address space hub vnet
Address space vnet02 (transitive vnet)
Address space hub vnet
Address space vnet02 (transitive vnet)
Spoke vnet is advertised with AS: 65001
It is visible the AS override
On-premises network